POWER TROWELS INSTRUCTIONS FOR USE

PT30

PLEASE BE SURE TO READ THIS MANUAL BEFORE STARTING YOUR OPERATION.

Special Warning

Please be sure to check the level of oil, as following:

1.The level of oil in engine, please be sure the level of oil is the range within the oil ruler scale. The engine would be shattered if the oil level is too low or without oil.   2.The level of oil in pedestal, please be sure the level of oil is below edge of the oil entrance. The speed-down machine would be shattered if the oil level is too low or without oil. Please close the fuel switch before stopping the engine if the engine will not be use for more one week, make the surplus oil be use out in the wasting oil container, because the oil is the volatilization liquid. It would remain the semisolid matter after volatilization. The wasting oil container might be jammed, and the engine can’t work normally.

Please be sure to read and know well the instruction and the details of the engine instruction and the operating regular. The maintenance and exact use is necessary in order to ensure person safety, extend useful life and reduce the troubles.

(You may match the machine indication to read the manual, it is concise and understandable.)

Foreword

It would be appreciated if you have bought our products.

The instruction is inform you how to use exactly and maintain the machines. Please be sure to read and know well related technology so that the machine can work in the good condition and extend the useful life.

Please fill the following information before using the machine in order to keep user’s advantage.

Product Type:                              No:

Engine No:                                No:

Please keep properly the guarantee card in order to make the maintenance record.

Catalog

Ⅰ  Sketch Map

Ⅱ  Safety Notice

Ⅲ  Check before using

Ⅳ  Turn on

Ⅴ  Turn off

Ⅵ  Simple Maintenance

Ⅶ  Trouble Shooting

Ⅰ. Sketch Map

Ⅱ. Safety Notice

Exhaust Notice

Can’t breathe in exhaust

Lease use the power trowel in the place with aerating all right.

Gasoline is flammable

Please stop the engine before putting on gasoline. Don’t add the gasoline too full and lean to using the machine

No smoking while you are putting on gasoline.

Defend High Temperature

Don’t touch muffler or coverwhen the machine is running or stopping. Don’t cover the machine by cloth or plastic while it is running.

Operator

Please the person unauthorized or which is not trained touch the equipment. Please check often the safe switch in order to keep safety.

Running Notice

As to operation and running components, please be sure to keep all safe equipments running without troubles.

Transport Notice

Please empty the engine gasoline when the machine are transported for far distance, in case the fuel machine can’t work.

Ⅲ. Check before using

Check the engine oil

Please put on machine oil first before using. Because the machine oil is drawn out before the products are leeave factory.

Check fuel

The product must use the normal lead-free gasoline.

Check the gear oil

Please put on gear oil before using. Because the gear oil is drawn out in the special status (air freight) when the products are transported.

Ⅳ. Turn on

- Open the flameout switch of engine to “ON”         2.Open safe switch to “ON”              3.Open fuel switch

4.Close block wind door               5.Put the oil door switch in                            6.One hand buttress handle,

middle position                                     another hand draw the engine

7.Warm up engine for three to five            8.Adjust blades to proper height            9.Two hands hold the handle, then

minutes first, then open block wind door                                              adjust the switch of oil door to proper

running speed for operation

Ⅴ. Turn off

- Put the switch door to “L”

- Put the safe switch to “Close”

- Put the blades to level position

Ⅵ. Simple Maintenance

Engine Section

Step:  Check and clear the air colander                       Step:  Check and clear the spark plug

Step:  Check and change the machine oil

Pedestal Section

Step:  Append and change the gear oil                                     Step:  Butter blade and under pan in case rust

Please maintain the machine termly refer to the work back-check table

Work Back-check Table

| Working Hours Components | (Day / Times) Every 8 Hours | ( Week / Times) Every 50 Hours | ( Month / Times )Every 200 Hours |
| --- | --- | --- | --- |
| A. Engine |  |  |  |
| 1. Machine Oil | Check | Change Oil |  |
| 2. Spark plug |  | Check |  |
| 3. Air Colander |  | Cleanout |  |
| B. Deceleration Machine |  | Check gear Oil | Check and Change Gear Oil |
| C. Blade Rest OilNib |  | Butter |  |
| D. Axletree lid Oil Nib |  | Butter |  |
| E. Strap |  | Check | Check or Change |
| F. Machine movement Point |  | Add a little engine oil |  |

Ⅶ. Trouble Shooting

| Ensure the reason of Troubles | The Way of Trouble Shooting |
| --- | --- |
| The engine can’t be turned on |
| 1. Flameout Switch of Engine | ON |
| 2. Safety Switch of Handle | ON |
| 3. Block Wind Door Switch of Engine | Open |
| 4. Fuel Switch | Open |
| 5. Lack fuel | Need Add Gasoline Fully |
| 6. Improper Fuel | Use Lead-free Gasoline |
| 7.Fuel is unclean | Clean up and Renew to Change Gasoline |
| 8. Air Colander is unclean | Clean up the air Colander |
| 9. Air Colander is wet | Change the air colander |
| 10. Cumulate Carbon in Spark plug | Clean out Cumulate Carbon |
| 11. The Gap of Spark Plug is improper | Adjust the gap(0.6-0.8mm) |
| 12. The type of Spark Plug is incorrect | Change |
| 13. Spark plug is wet | Clean up and draw many times |
| 14. Circuit Test (Enclose Picture A) |  |
| Spark is too small | Change |
| Without Spark | Check Circuit |

| Ensure the reason of Troubles | The Way of Trouble Shooting |
| --- | --- |
| The engine can’t be turned on |
| 15. Test Oil Route(Enclose Picture B) |  |
| Drop Fuel | Lock Fixation Button |
| Drop fuel and Water | Clean up the Oil container and Wasting Gasoline Machine |
| Don’t drop fuel | Professional person deal with the Wasting Gasoline Machine or Contact us |
| The Power of Engine is precarious |
| 1. Wasting Gasoline Machine is blocked | Professional person deal with the Wasting Gasoline Machine or Contact us |
| 2. Speedup pole is not orientated | Professional person deal with the Wasting Gasoline Machine or Contact us |
| The speed of Engine is too slow |
| 1. Gasoline door line is improper position ( Enclose Picture C ) | Adjust the Gasoline door line to proper position and fix up it or change |
| It is very exertive to start up the handle |
| 1. Gasoline door line is improper position | Adjust the Gasoline door line to proper position and fix up it |
| 2. The speed of engine is too high | Adjust the engine |
| 3. Clutch trouble | Check or change |

| Ensure the reason of Troubles | The Way of Trouble Shooting |
| --- | --- |
| The engine can’t be turned on |
| Drive is Good (Enclose Picture D) |
| 1. The Strap is abraded | Change |
| 2. Strap wheel is abraded | Change |
| 3. Strap wheel is improper position | Adjust and fix up |
| 4. Strap skid | Check and Change the Clutch |
| 5. Strap wheel of Pedestal drive primly | Contact us |
| The angle of blades is improper |
| 1. The tightwire of handle is loose | Fix up the tightwire newly or change |
| 2. The blade rest run primly | Maintain and Change |
| 3. The platen run primly | Maintain and Change |
| It is not good to operate and control the machine |
| 1. The position of blades are improper | Fix up newly |
| 2. The blades are fixed incompletely | Fix up completely |
| 3. The ridge of blades are leaned | Change |
| 4. The blades are uneven | Change |
| 5. The ridge of blades are uneven | Change |
| 6. The blades are not changed at the same time | Change newly |
| 7. The pedestal are proofread hardly | Contact us |
| Note: Please contact the After-sales Service Department or the local distributor if you have any further question. |
| Services phone( 24 hours every day ): |